## Slide 1: Students Recordings category: Classical Recording
Technical University of Gdansk
Sound Engineering Department

## Slide 2: Recording Material
composition:
“Gloria” - part I Gloria, Antonio Vivaldi
performers:
Choir “Cantores Veiherovienses” and cameral orchestra “Musica Camerata”
place:
Holly Trinity Church in Wejherowo, Poland

## Slide 3: Recording team
producer
  Piotr Odya
recording
  Jarosław Derewecki
  Piotr Nowiński
mastering
  Rafał Lerch
  Bartłomiej Podleś

## Slide 4: Recording Conditions
live recording, concert,
large church with long reverberation time about 5 seconds,
hard walls made of stone - strong reflected, not many diffusors,
performers placement

## Slide 5
CHOIR
ORCHESTRA
CONDUCTOR
AB system
2 omnidirectional microphones Neumannn KM83
in distance 1 m and 1 m between them, 2,62 m high
XY system
1 stereo microphone Neumann 69fet
8 m away from the conductor
2,30 m high
1 m
Performances and microphones placement
8 m

## Slide 6: Description of the System
AB system with the additional microphone for natural reverberation,
digital YAMAHA O1V console,
multitrack recording system with ADAT XT20 (20-bits 48 kHz),

## Slide 7: System diagram

## Slide 8: Discussion -advantages
quantity
clarity
wide space
tone balance between the choir and orchestra

## Slide 9: Discussion -disadvantages
unequal reverberation of choir and orchestra
small compatibility with mono-stereo because of using AB system